Product Specification

Product Class: LED Lens

Item No: DK-5050-30-LENS-4H1-H8.5-XPE

Material: PMMA

Certification: RoHS

Sut Up:Xuan Yang

Check:Xiaohui Liang

Page 1                     March 9,2016

Content

Specification---------------------------------------------------------------3

2D Drawing----------------------------------------------------------------4

Optical Datasheet--------------------------------------------------------5

Packing---------------------------------------------------------------------6

Application Notes---------------------------------------------------------7

Page 2                      March 9,2016

Specification

| Item No | Picture | Size | Matched LED | Lighting Application |
| --- | --- | --- | --- | --- |
| DK-5050-30-LENS-4H1-H8.5-XPE |  | diamete: 50x50mm height:8.65mm FWHM:30° | 3535 | LED High Bay Light |

Page 3                      March 9,2016

Drawing

Page 4                      March 9,2016

Optical Test Report

Page 5                       March 9,2016

Packing

| Material | Size | Total |
| --- | --- | --- |
| Antistatic blister box | 4W | 20PCS a layer or deck |
| Box | 335*245*105mm | 220PCS/ Box |
| Outer Box | 510*330*255mm | 880pcs/ Outer Box |

Page 6                      March 9,2016

Application Notes

- Please use a litter water and soft fabric (air-laid paper) to clean the lens &           reflector if necessary.

- Forbid to use industrial solvent to clean the lens, such as alcohol.

- The working temperature is -40ºC～+80ºC.

- Storage environment temperature is 0ºC～40ºC，humidity is 30%~95%。

Optic Lens has the function to change the ray of light, it is made of optical material, the effect shall be influenced once pollute. Please do not open the packing before use it，to avoid the dust pollution.

- Protect the product from the sun and other ultraviolet ray, as these will lead to aging, change color, crack, etc.

- Please ware gloves once install the lens, avoid to abrasion the lens surface.

（7）Forbid to use acidic or alkaline solution touch the product, avoid to generate the chemical reactions.

Page 7                    March 9,2016